OVERVIEW.DOC 02/11/80

O O O	O O O	O O O	O O
O   O	O	O   O	O   O
O O O	O O	O O O	O   O
O O	O	O   O   O   O
O   O	O O O	O   O	O O

	O   O	O O O
	OO OO	O
	O O O	O O
	O   O	O
	O   O	O O O

O O O	O O O	O O O	O O O	O O O
O	  O	O   O	O 	  O
O O	  O	O O O	O O O	  O
O	  O	O O	    O	  O
O	O O O	O   O	O O O	  O


     Here's a quick overview of CBBS.  It's just the thoughts �
off the top of my head.

					Ward.


CBBS is designed to work with S-100 modems, but there should be�
no troubles using it with outboard modems.

Steve Vinokuroff of Vancouver B.C. Canada has been the first to�
try it, as well as double density. I have put together another�
module, CBBSMODM.ASM which is a skeleton for using CBBS with an�
outboard modem.  I plan to test it locally using my serial�
port, and my sense switch to simulate two bits in: carrier�
detect, and ring detect.

CBBS will work with 1 disk, 2 is better.  The bigger the�
better, up to a point, where you might have so many messages on�
the disks that it takes a new user too long to go thru the�
summaries.  Randy and I keep about 300 messages active on�
CBBS/Chicago, and that seem OK.  200 would probably also be OK. �
We find 300 is the number that "happens" due to a 2-month-old�
message delete policy.

CBBS currently has no auto-delete.  With clocks becoming more�
prevalent, perhaps that's not so hard to do, some time in the�
future.

Feedback:  It's important.  If you find bugs, or have �
additions which you think might be of general interest to other�
CBBS operators, let us know.  You may contact me by mail at:

	Ward Christensen
	688 E. 154th St.
	Dolton, Il. 60419
	(312) 849-6279


If you have hardware, backup, distribution, etc. questions,�
contact Randy:

	Randy Suess
	5219 W. Warwick
	Chicago Il 60641  	(312) 545-7535


Our CBBS works as follows thanks to a "kludge" board Randy put�
together.  He also put a solid state relay on the diskette�
drive spin motors.  We hear the main bearing is the first thing�
to go out on a disketton, but we have not had that happen, to the best of our�
knowledge, in over 50,000 calls.

		  ----------------

What's nextging from�
resetting the system again, and starts the diskette drive spin�
motors.  We are using a Tarbell single density controller, and�
the reset causes it to boot.  We just converted to CP/M 1.4.�
The BIOS would require major mods if you have 2.0.  We have�
modified the CP/M BIOS so that, on cold boot, rather than just�
JMPing to CCP, if sense switch 80H is up (we put a SSW on a�
parallel port, using a dip-switch 'cause we had no front�
panel), then CBBS.COM is loaded and branched to.  (CBBS was�
originally called "CE" or "CE.C" so that's where some such�
names come from, such as "CEBIOS.ASM").

That technique was required with 1.3, but now with 1.4, you can�
autoboot into CBBS by patching CBBS into the command buffer at�
CCP+8, and a hex 04 (the length of the word "CBBS") into CCP+7.

Booting in CBBS takes less than 30 seconds (but long enough�
that a few users have had to modify their terminal programs,�
which time out due to the number of rings before CBBS answers).

When CBBS gets control, it outputs to a control port, which the�
kludge board decodes, and thus leaves the spin motors on.  Thus�
the 30 second one shot is or-ed with this output port, to�
determine if the motors are to spin or not.

CBBS then issues the output commands to take the modem off­
hook, and put out carrier.

We then wait 15 seconds for the incoming carrier. If you have a�
baud-rate-settable modem, we then set to 110, and go read a�
character.  If it's a carriage return (C/R) then we continue at�
110 baud.  We use 2 stop bits at 110, and 1 at all higher�
rates.  We don't bother with parity, and send 8 full data bits,�
to allow future expansion to where you might want to transfer�
fully transparent binary data via CBBS (such as when we use a�
modem transfer program).

The baud rate is switched to 300, 450, then 600, to 110 (at the�
"end" of 600), then back to the beginning, 110, each time�
reading a character to see if it is a C/R.  15 loops are made�
(75 characters read in all) before giving up.  When we give up,�
we output to the control port again to turn off the spin�
motors, output to the modem to hang up the phone, and then JMP�
up to a PROM monitor, which does nothing.  We could just as�
well have gone into a loop in CBBS, because the next phone ring�
would reset the system, and start things all over again.

We also do a double read of the C/R to make sure a glitched�
character isn't interpreted as a C/R at the wrong speed.

		----------------

Not all users will elect to put together such functions as�
Randy did, and will instead choose to run CBBS memory resident. �
An equate, REINIT, allows this, if set true. All the flags�
(upper case mode, operator mode, etc) are reset, and CBBS loops�
looking at ring detect.

		----------------

If you do not choose to use our BIOS, then you will have to�
make your own, which need follow only these guidelines:


The console I/O functions (status, console in, console out)�
must check the modem.  You may elect to check your local�
console I/O also, as we did.  This allows the CBBS operators to�
converse with callers if they find them in trouble, or find a�
friend on the system, etc.  This is all pretty standard coding. �
Examples may be found in CEBIOS.ASM on the diskette.

The only non-standard thing in the BIOS is the carrier detect.  
To prevent CBBS being hung up at console in with a loss of�
carrier, return TRUE (0FFH) from status, if carrier is lost,�
and also return 0FFH from console in, if carrier is lost.  
Do not do a WAIT to see if it's a temporary glitch, CBBS will�
wait 1 second before looking again.  Don't just take control�
away from CBBS, as it might be in the middle of a disk write,�
such as if someone hangs up while leaving comments.  We set�
flags saying carrier is lost, and test a flag saying we can't�
go away just now, until the disk is properly closed.  (Comments�
elsewhere explain how "BYE" thus could present problems)

Conceivably, someone could hang up, such as during writing�
comments, and another person call up and reset the system too�
soon, but we have not had that happen, to the best of our�
knowledge, in over 50,000 calls.

		  ----------------

What's next?  Get a listing of all the CBBS .ASM files, as well�
as all the .DOC files, and go thru COOKBOOK.DOC.  You will be�
expected to make some changes to the .ASM files, to tailor them�
to your environment, or just to change references to "Ward and�
Randy", and to "CBBS/Chicago.

It is my intent to ship a working CBBS.COM for just "dinking�
around" with CBBS, i.e. entering messages, trying the operator�
functions, etc.  We will include some messages which you might�
like to pattern your own after, such as the one on expert user�
mode, etc.  We recommend setting the starting message number�
perhaps at 20, or perhaps 100, as this leaves some "permanent�
system message" area open from 1-19.

This test CBBS is a 1 disk version, which you may use to �
familiarize yourself with CBBS operation.  

The test version of CBBS is supplied with the operator-mode�
flag already set.

The operator password is "CBBSPASS", so type in function PASS�
and when system responds with a C/R (but no other prompt), just�
type CBBSPASS.  If it didn't work, it will log a "security�
failure" to the log, and tell you it didn't know what you mean�
by "PASS".


		  ----------------

		What to watch for:

As you will learn from reading the CBBS .ASM files, CBBS is not�
some elegant, efficient, well written piece of programming�
artistry.  It's more like a software patchwork quilt, with�
things tacked on here and there.  No attempt at structured�
programming was done.  I did pull out some obvious duplication�
of code in some places.  It is moderately commented, enough�
that anyone familiar with CP/M and 8080 assembler, who wants to�
get CBBS up, can and did. 

CBBS had one goal in mind - that it be relatively simple.  The�
main .ASM files are not over 8000 lines, but I still feel that�
is true:  there are no fancy data structures on the disk.  All�
files are editable with any standard CP/M editor (ED,�
Wordmaster).  The only minor thing is the use of a bell (07H)�
delimiter for messages in the message files and the summary�
file. "[" and "]" have certain meanings in other files.

The ORIGINAL CBBS organized it's message and summary files as�
follows:  10 messages were written to each message file.  The�
name of the file was MESSAGE.nnX, i.e. message 133 was in file�
MESSAGE.13X.  Similarly, the summary file was one per 100�
messages, and the name was SUMMARY.nXX, such as SUMMARY.1XX for�
summaries 100-199.  That made things quite easy.  Want to�
summarize starting at message 123? Just open file SUMMARY.1XX,�
scan for "(bell)123" and start typing.  Want to kill a message? �
Just read the appropriate summary file into memory, delete from�
(bell)nnn thru the next bell header, erase the summary, make�
it, and write it back from memory.  This was quite fast.  Same�
logic applied to the message file, except that instead of just�
compressing it out of memory, it was written to the tail-end of�
"KILLED" file, so operators could see short-lived messages, or�
messages which were mischievously killed. 

Ok, what's the problem?  Well, when we got up around 550�
(numbers, not active), then there weren't enough directory�
entries available.  Each file, whether it contains only 1�
message, or all 10 were still present, took a directory entry.

Messages had to be packed every now and then (as often as�
weekly, on a busy system).  This was an inconvenience to users,�
as message 524 would become 219 or some such, and they couldn't�
tell where to pick up from the last time they called in.  Also,�
someone would leave a message which says "in regard to your�
message 524" which would not be 524 after the pack.

So, in July 1979, portions of CBBS were rewritten, and the�
package given the name "version 3".  Message numbers went to 5�
digits, and would never be reused or packed. Later, keeping�
track of the necessary subroutines, and have overlays for�
entry, kill, summary, etc.  Then CBBS could easily be extended. �
I still have thhe disk, to count the lines in the summary file. �
(T SUMMARY #)  This, divided by 2, should be the number of�
active messages stored at the third parameter in the file�
"NEXT".  Alternatively, BUILDSUM will TELL you the number.

The simplicity of the file name selection which was used for�
the previous version, was similar in version 3 for message�
files, except that the low order digits of the message number�
was used.

For example, message 1234 would be written to file MESSAGE.X34. �
Message 1235 was also written to this file, because CBBS did an�
integer divide of 35 by 2, getting 17, then multiplied by 2,�
getting 34.  This is done in routine "SETMSGN".  We tried a�
"ANI" technique with a mask over the low ASCII digit of the�
file number, but that didn't work too well, so we went to the�
divide-and-multiply technique.  On a double density system with�
128 entries in the directory, you might want to go to having�
100 message files, by setting FILEDIV to 1.  This will�
significantly speed up both retrieve, and kill.

This technique spread the messages around nicely. No message�
file got out of hand size-wise.

Unfortunately, I was unable to come up with a similarly simple�
approach for the summary file.  I admit fancy techniques could�
be used, such as an "indexed" random-access approach, but�
remember the "S" and "Q" command search the summary�
sequentially, and you don't want performance of these commands�
to suffer.

What's the problem?  Well, writing the summary files to �
SUMMARY.nXX won't work, as summary numbers can take any value�
from 00001 to, well, however many messages a given CBBS will�
ever get!  CBBS/Chicago is currently at message 10200.  Thus,�
to make "S" and "Q" work quickly, I went to a single summary�
file.  This caused a problem, since it might be too big to fit�
into memory, during the kill.  Other than this, there would be�
no need to have more than 24K in a CBBS system.  So, Kill now�
works as follows, (instead of the read in, erase, write back�
like before):  The summary is flagged, and the operators, under�
operator mode, use a new PURGE command to pass the summary thru�
memory once to delete ALL flagged summaries.

		  ----------------

I have written a BUILDSUM program to reconstruct the summary�
file.  Also supplied is a crude CONVERT.ASC program to convert�
previous CBBS files to the new format.  I'm sorry that it only�
works when generating 50 message files. I'll try to come up�
with a new more generalized one, if you old-CBBS operators ask�
hard enough for it. (No one has - so I won't)

		  ----------------

The future of CBBS:  Lots of people are interested in CBBS type�
systems sharing messages.  That is of course quite hard to�
manage, due to the cost of long distance phone calling.  Also�
it's difficult to determine which messages are eligible for�
forwarding.  Do you just take all that ask to be forwarded, or�
have a file of people who are allowed to forward?  ..or build a�
file of message numbers which have been asked to be forwarded,�
then as operators, validate the list?  Wow, many more questions�
than answers.

Some CBBS systems might like to go to a mailbox system for�
certain users;  Others might like to add a feature which keeps�
track of a caller's last time called, i.e. high message number,�
date called, etc.  There is certainly no limit to the ideas�
which can be thought up, just a limit to who has the time and�
energy to implement them.

A totally new generation of CBBS software, I feel, would have�
to be based around more of a "transaction monitor" like the big�
computer systems have, i.e. rather than CBBS having to be a�
gigantic program, there could be a monitor which brings in the�
needed pieces as overlays.  Conceptually this is not difficult. �
It could be done by re-writing CCP to be the monitor, and have�
it call in .COM files on request.  The problem would be sharing�
common subroutines, such as those file-related ones in CBBS�
like EXTEND, SETRD, RDBYTE, etc.  

This would probably be most easily done by making a ROOT CBBS�
with all the necessary subroutines, and have overlays for�
entry, kill, summary, etc.  Then CBBS could easily be extended. �
I still have this idea in the back of my mind, but it will take�
quite a bit of time to convert it.  Another problem is that�
each overlay will take another directory entry, and with 50�
message files already (could go to less?) the directory of a�
single density disk would not be enough.

It does sound intriguing, maybe someday it will happen.  I �
particularly like the idea since, for example, private�
mailboxes, or program download could be implemented more�
easily.

	  --------------------------------

Thanks for buying CBBS.  The $50 goes to keeping CBBS/Chicago�
alive and well, (just bought new drives after 3 years of use)
but of course doesn't come close to paying for it. 

Please feel free to contact Randy or me if you have questions�
or suggestions.  If there are any glaring holes in the�
admittedly meager documentation, let me know.  It will be�
improved on a time- and energy- available basis.  Any and all�
suggestions, are greatly appreciated.  Hmmm, let me qualify�
that - I enjoy hacking up CBBS to add new things.  I solicit�
"ideas", but am not really interested in "code".  "Not Invented�
Here"?  Mebbe, or perhaps its that I'm a "loaner", and�
accepting some mods, means I'd have to accept "them all", and�
programming "by committee" just doesn't work out - one person�
extends something, another extends something else; there is�
some overlap, new mods aren't based on the same base, etc.  

YOU should feel free to "hack up" CBBS to be whatever you want�
it to be - perhaps make you changes "modular" to facilitate�
integrating them into a possible future release of CBBS.

				Thanks,
				Ward Christensen
				11/28/81